## Slide 1: LSTM-BASED APPROACH FOR GENERATOR STATE PREDICTION IN TRANSIENT STABILITY ASSESSMENT AND CONTROL USING TRANSIENT ENERGY FUNCTION
Presented By:
Bhupesh Jaishi (078BEL026)
Binod Kumar Sah (078BEL030)
Bishal Chaurasiya (078BEL031)
Chandan Sah (078BEL032)
Supervisor :
Associate Professor Jeetendra Chaudhary
DEPARTMENT OF ELECTRICAL ENGINEERING
IOE, PULCHOWK CAMPUS

## Slide 2: Introduction
Power System stability refers to the system's ability to return to normal or stable operation after having been subjected to some form of disturbance.
Transient stability involves the response to large disturbances, which may cause large change in rotor angle and speed leading to cascading failure of the system.
Transient stability assessment methodologies are broadly classified into three main types:
Simulation Methods (Time-Domain Simulation)
Direct Methods (Energy Function based)
Data-Driven Methods (Machine Learning based)

## Slide 3: Swing Equation and State-Space Formulation
Swing Equation:
State-Space Representation:
Sate Variables:
Hence Power system dynamics is described by the state space as:
Introduction

## Slide 4: Lyapunov Function
A Scalar function which describes the total energy of the system.
Stability Criteria: 1. V(x)>0, for all x not equal to xs
2.
Transient Energy function Described for post fault system, given by :
Introduction

## Slide 5: Literature Review
Our project is founded on the real-time prediction and control framework proposed by Bhui and Senroy [1].
They have used Transient Energy function Frame work to make assessment of transient Stability by Dividing the computation into two mode of computation
a.Offline Computation
b.Online Computation
They have developed fast and robost framework for stability assessment. In Offline Phase Boundary of Controlling Unstable Equillibrium Point (BCU) method Integrated with Potential Energy Boundary Surface (PBES) method to find mode of disturbance (MOD) and normalized kinetic energy vector for lookup table
PEBS and BCU and are two different Algorithmic technique which utilizes the transient energy function for finding critical energy and critical clearing time.
PEBS involves computation of Fault on trajectory of the system and detect the highest potential by monitoring at each time steps.
BCU method uses PEBS result as initial condition

## Slide 6: Literature Review
In the online stage of the paper correct MOD is identified and energy margin (Vcr-Vcl) is calculated to find the stability of the system.
Control action is taken if system is found unstable by shading the appropriate generation from the system. There is need of prediction of generator angle and speed at the time of generation shedding accounting for computational delay.
The minimum amount of data available for this prediction corresponds to the computational delay associated with the application of the TEF technique , signal latency and initiating control actions delay.
Quadratic and cubic curve fitting have been used for predicting the angle which is produces error[1]

## Slide 7: Problem Statements
Error in the prediction of rotor angle and speed:
Inaccurate prediction of rotor angle and speed lead to inaccurate generation shedding.
System May remain unstable.

## Slide 8: Objectives
• To develop and implement an LSTM (Long Short-Term Memory) neural network model for accurate, real-time prediction of generator angles and speeds in the IEEE 39 bus system following a fault
• To integrate the generator state predictions into the Transient Energy Function (TEF) framework for improved transient stability assessment and control.
• To demonstrate the applicability of the enhanced TEF method on the IEEE 39-bus test system

## Slide 9: METHODOLOGY

## Slide 10: METHODOLOGY
Estimation of Amount of Control Actions Required and Monitoring of Stability Status
Step 1 : Prediction of generator speed and angles[LSTM]
Step 2 : Modification in Energy Function for Generation Shedding
Step 3 : Estimation of the amount of Control action required

## Slide 12: System Under Consideration

## Slide 13: Result And Analysis
Fault At bus 7 at t=0 and cleared at 0.15 |  |  | 
Result | TDS | BCU | PEBS
V | Vcl =0.843 | Vcr_BCU=0.973 | Vcr_PEBS=1.25
Critical clearing time (Tcl) | Tcl=0.15 | Tcr_BCU=0.162 | Tcr_PEBS=0.184
Computation Time | 0.14 | 0.15 | 0.12
Transient Energy Function and BCU Results From MATLAB
Transient energy function framework is developed for IEEE-9 bus system using classical model consideration. Fault at bus 7 is created and results obtained is compared with the Saur and Pai result shown in the table below:
Result 1
Vcr_PEBS > Vcl
Tcr_PEBS >Tcl System is PEBS Stable
Vcr_BCU> Vcl
Tcr_BCU>Tcl System is BCU Stable
Fig 8: w vs del for faulted and Post fault Dynamics (Stable)

## Slide 14: Result And Analysis
Fault At bus 7 at t=0 and cleared at 0.2 |  |  | 
Result | TDS () | BCU | PEBS
V critical | Vcl=1.473 | Vcr_BCU=0.973 | Vcr_PEBS=1.25
Critical clearing time (Tcl) | Tcl=0.2 | Tcr_BCU=0.162 | Tcr_PEBS=0.184
Computation Time | 0.21 | 0.06 | 0.05
Vcr_PEBS< Vcl
Tcr_PEBS<Tcl System is PEBS Unstable
Vcr_BCU<Vcl
Tcr_BCU<Tcl System is BCU Unstable
Result 2
Fig 10: w vs del for faulted and Post fault Dynamics (Unstable)

## Slide 15
Fig 11: del vs t and w vs t for faulted and
Post fault Dynamics (Unstable)
Fig 9: del vs t and w vs t for faulted and
Post fault Dynamics (Stable)
Result And Analysis

## Slide 16
Time Domain Simulation Using PSS/E :
Fault created at Bus 29 at t=1.0 and cleared at t=1.4.
Generator G9 goes out of synchronism.
Output 1:
Plot 1[time vs rotor angle]
Result And Analysis
Plot 2 [time vs speed]
Output 2:
Fault created at Bus 29 at t=1.0 and cleared at t=1.4.
Generator G9 goes out of synchronism.
Gen9
Gen9

## Slide 17
Matlab
Python
PSS/E
Network Modeling:
For the development of the TEF Internal node model is developed using the constant impedance load and internal node behind the transient reactance is used followed by Kron’s reduction to show the coupling between the generators. For the development of the real system all the parameters are included.
Generator Modeling: Classical Model for TEF and Detailed Model in real time simulation in PSS/E
Disturbance Type: 3-Phase Symmetrical Fault
Scope
Tools and software used

## Slide 18
Lookup Table
LSTM
Model Training
Integration of LSTM with TEF for control action
Testing & Validation:
Documentation
Remaining Work

## Slide 19
TEF Framework for IEEE-9 Bus is developed and Stability is analyzed in the result section.
IEEE39 bus system is completely developed in PSSE
Result for the different fault location has been analyzed at current stage in IEEE 39 Bus system using PSSE along with Training Data Collection
Conclusion

## Slide 20: References
[1] P. Bhui and N. Senroy, "Real Time Prediction and Control of Transient Stability Using Transient Energy Function," IEEE Trans. Power Syst., doi: 10.1109/TPWRS.2016.2564444.
[2] F. Silva-Rodriguez, H. Raffoul, and Y. Li, “LSTM-Based Net Load Forecasting for Wind and Solar Power-Equipped Microgrids,” in Proceedings of the 2024 IEEE Power & Energy Society General Meeting (PESGM), Seattle, WA, USA, Jul. 2024, pp. 1–6. doi: 10.1109/PESGM56776.2024.1234567.
[3] G. Van Houdt, C. Mosquera, G. Nápoles, “A review on the long short term memory model,” Artificial Intelligence Review, vol. 53, pp. 5929 5955, 2020.
[4] H. D. Chiang, F. Wu and P. Varaiya, “A BCU method for direct analysis of power system transient stability,” IEEE Trans. Power Syst., vol. 9, pp. 1194–1208, Aug. 1994.
[5] P. W. Sauer, M. A. Pai, and J. H. Chow, Power System Dynamics and Stability, Second Edition. Hoboken, NJ, USA: John Wiley & Sons Ltd, 2018.

## Slide 21: Thank You!